## Slide 1: Homework-Ch4

## Slide 2
4-1. A group of N stations share a 56-kbps pure ALOHA channel. Each station outputs a 1000-bit frame on average once every 100 sec, even if the previous one has not yet been sent (e.g., the stations can buffer outgoing frames). What is the maximum value of N?
With pure ALOHA, the usable bandwidth is 0.184×56 kbps = 10.3 kbps. Each station requires 10 bps, so N = 10300/10 = 1030 stations.

## Slide 3
4-2. A large population of ALOHA users manages to generate 50 requests/sec, including both originals and retransmissions. Time is slotted in units of 40 msec.
(a) What is the chance of success on the first attempt?
(b) What is the probability of exactly k collisions and then a success?
(c) What is the expected number of transmission attempts needed?
With 25 slots/second and an average of 50 requests/second, we have G = 2.
Then use the slotted Aloha formulas in Sec. 4.2.1.
(a) With G = 2 Poisson’s Law gives a probability of e-2.
(b) (1 - e-G)k e-G = 0. 135 × 0. 865k.
(c) The expected number of transmissions is eG = 7. 4.

## Slide 4
4-3. What is the length of a contention slot in CSMA/CD for
(a) a 2-km twin-lead cable(signal propagation speed is 82% of the signal propagation speed in vacuum)?, and
(b) a 40-km multimode fiber optic cable (signal propagation speed is 65% of the signal propagation speed in vacuum)?
(a) Signal propagation speed in twin lead is 2. 46 × 108 m/sec. Signal propagation time for 2 km is 8.13 μsec. So, the length of contention slot is 16.26 μsec.
(b) Signal propagation speed in multimode fiber is 1. 95 × 108 m/s. Signal propagation time for 40 km is 205.13 μsec. So, the length of contention slot is 410.26 μsec.

## Slide 5
4-4. Consider five wireless stations, A, B, C, D, and E. Station A can communicate with all other stations. B can communicate with A, C and E. C can communicate with A, B and D. D can communicate with A, C and E. E can communicate A, D and B.
(a) When A is sending to B, what other communications are possible?
(b) When B is sending to A, what other communications are possible?
(c) When B is sending to C, what other communications are possible?
·A
·B
·C
·D
·E
For successful communication we require that the sender can reach (communicate with) the receiver, and that there be no other sender who can reach (now interfere with) the receiver. Also, a station cannot send and receive at the same time.
(a) no other communication is possible.
(b) no other communication is possible.
(c) E can safely send to D since it will not interfere with C’s reception.
Notes: For successful communication we require that the sender can reach (communicate with) the receiver, and that there be no other sender who can reach (now interfere with) the receiver. Also, a station cannot send and receive at the same time.
(a) Since all stations will see A’s packet, it will interfere with receipt of any other packet by any other station. So, no other communication is possible in this case.
(b) B’s packet will be seen by E, A and C, by not by D. Thus, E or C might try to send to D at the same time. However, E and C can communicate with A, so this would interfere with B’s transmission to A. Thus no other communication is possible.
(c) B’s packet will be seen by E, A and C, by not by D. Thus, E or A might try to send to D at the same time. Of these two possibilities, A can communicate with D, so this would interfere with B’s transmission to A. But E can safely send to D since it will not interfere with C’s reception.

## Slide 6
(a) A给B发送数据，BCDE均在A的覆盖范围内。CDE若收数据，则会同时收到A发送的数据，故不可能存在其他通信。
(b) B给A发送数据，ACE在B的覆盖范围。
CE不能作为接收者收数据，否则会同时收到B发送的数据（被干扰）
CE作为发送方给A发送数据，会对B给A发送的数据造成干扰
C作为发送方给D发送数据，C覆盖ABD，会造成A被干扰
E作为发送方给D发送数据，E覆盖ABD，会造成A被干扰
(c) B给C发送数据，ACE在B的覆盖范围。
AE不能作为接收者收数据，否则会同时收到B发送的数据（被干扰）
AE作为发送方给C发送数据，会对B给C发送的数据造成干扰
A作为发送方给D发送数据，然而A覆盖BCDE，会造成C被干扰
E作为发送方给D发送数据，E覆盖ABD，不会干扰C
·A
·B
·C
·D
·E

## Slide 7
4-5. A 1-km-long, 10-Mbps CSMA/CD LAN (not 802.3) has a propagation speed of 200 m/μsec. Repeaters are not allowed in this system. Data frames are 256 bits long, including 32 bits of header, checksum, and other overhead. The first bit slot after a successful transmission is reserved for the receiver to capture the channel in order to send a 32-bit acknowledgement frame. What is the effective data rate, excluding overhead, assuming that there are no collisions?
The round-trip propagation time of the cable is 10 m sec. A complete transmission has six phases:
1. Transmitter seizes cable (10 m sec)
2. Transmit data (25. 6 m sec)
3. Delay for last bit to get to the end (5. 0 m sec)
4. Receiver seizes cable (10 m sec)
5. Acknowledgement sent (3. 2 m sec)
6. Delay for last bit to get to the end (5. 0 m sec)
The sum of these is 58. 8 m sec. In this period, 224 data bits are sent, for a rate of about 3.8 Mbps.

## Slide 8
4-6. An IP packet to be transmitted by Ethernet is 60 bytes long, including all its headers. If LLC is not in use, is padding needed in the Ethernet frame, and if so, how many bytes?
The minimum Ethernet frame is 64 bytes, including both addresses in the Ethernet frame header, the type/length field, and the checksum.
Since the header fields occupy 18 bytes and the packet is 60 bytes, the total frame size is 78 bytes, which exceeds the 64-byte minimum. Therefore, no padding is used.

## Slide 9
4-7. Consider building a CSMA/CD network running at 1 Gbps over a 1-km cable with no repeaters. The signal speed in the cable is 200,000 km/sec. What is the minimum frame size?
For a 1-km cable, the one-way propagation time is 5 µsec, so 2τ=10 µsec. To make CSMA/CD work, it must be impossible to transmit an entire frame in this interval. At 1 Gbps, all frames shorter than 10,000 bits can be completely transmitted in under 10 µsec, so the minimum frame is 10,000 bits or 1250 bytes
L/B >= 2D
L/1Gbps >= 2*1km/200000 km/s
L = 10000 bit

## Slide 10
4-8. Consider the extended LAN connected using bridges B1 and B2 in Fig. 4-33(b). Suppose the hash tables in the two bridges are empty. List all ports on which a packet will be forwarded for the following sequence of data transmissions:
(a) A sends a packet to C.
(b) E sends a packet to F.
(c) F sends a packet to E.
(d) G sends a packet to E.
(e) D sends a packet to A.
(f) B sends a packet to F.
(a) B1 will forward this packet on ports 2, 3, and 4. B2 will forward it on 1, 2, and 3.
(b) B2 will forward this packet on ports 1, 3, and 4. B1 will forward it on 1, 2, and 3.
(c) B2 will not forward this packet on any of its ports, and B1 will not see it.
(d) B2 will forward this packet on port 2. B1 will not see it.
(e) B2 will forward this packet on port 4 and B1 will forward it on port 1.
(f) B1 will forward this packet on ports 1, 3, and 4. B2 will forward it on port 2.

## Slide 11
4-9. Store-and-forward switches have an advantage over cut-through switches with respect to damaged frames. Explain what it is.
Store-and-forward switches store entire frames before forwarding them. After a frame comes in, the checksum can be verified. If the frame is damaged, it is discarded immediately.
With cut-through, damaged frames cannot be discarded by the switch because by the time the error is detected, the frame is already gone. Trying to deal with the problem is like locking the barn door after the horse has escaped.

## Slide 12
4-10. It is mentioned in Section 4.7.3 that some bridges may not even be present in the spanning tree. Outline a scenario where a bridge may not be present in the spanning tree.
All bridges do participate in the spanning tree algorithm and compute a path towards the root.
However, some bridges may not be part of the spanning tree that is used to forward frames between stations.
In particular, a bridge that does not have any station directly connected to any of its ports and is part of a loop is a candidate for not being a part of the spanning tree used for forwarding. This can happen if the shortest paths to the root for all bridges connected to this bridge does not include this bridge.

## Slide 13: End